## Slide 1: Antikernel A Decentralized Secure Hardware-Software Operating System
Andrew Zonenberg (@azonenberg)
Senior Security Consultant, IOActive
Bülent Yener
Professor, Rensselaer Polytechnic Institute
This work is based on Zonenberg’s 2015 doctoral dissertation, advised by Yener.

## Slide 2: Kernel mode = full access to all state
What OS code needs this level of access?
  Memory manager only needs heap metadata
  Scheduler only needs run queue
  Drivers only need their peripheral
  Nothing needs access to state of user-mode apps
No single subsystem that needs access to all state
Any code with ring 0 privs is incompatible with LRP!

## Slide 3: Monolithic kernel, microkernel, …
Chart: 
| Monolithic | Micro | ???
Privileged Software Size | 2 | 1 | 0
Ring-0 code size
Huge
None
Small
Huge attack surface
Can we get here?

## Slide 4: Exokernel (MIT, 1995)
OS abstractions can often hurt performance
  You don’t need a full FS to store temporary data on disk
Split protection / segmentation from abstraction
OS does very little:
  Divide resources into blocks (CPU time quanta, RAM pages…)
  Provide controlled access to them
Drivers can be microkernel-esque servers

## Slide 5: But wait, there’s more…
By removing non-security abstractions from the kernel, we shrink the TCB and thus the attack surface!

## Slide 6: So what does the kernel have to do?
Well, obviously a few things…
  Share CPU time between multiple processes
  Allow processes to talk to hardware/drivers
  Allow processes to talk to each other
  Page-level RAM allocation/access control

## Slide 7: Are you sure?
Barrel proc / HT can context switch without S/W help
What if we moved the whole run queue into the CPU?
PID 1
PID 2
PID 3
PID 4
PCs[]
FETCH
Reg file
DECODE
EXECUTE

## Slide 8: Hardware scheduler
Circular queue of thread IDs = round robin scheduler
Minimal gate count (one small small FIFO)
Deterministic performance (good for hard realtime)
No possibility of corrupting unrelated state

## Slide 9: Access to hardware
Instead of a bus, connect the CPU to rest of the SoC with a packet-switched NoC
  Assign addresses as {cpu subnet prefix, PID}
CPU ::8040/10
Mgmt ::8040/16
App1 ::8060/16
App2 ::8061/16
RAM ::8003/16
Flash::8004/16

## Slide 10: Communication
Two parallel networks
  RPC network: 4x 32 bit words, ≈ ioctl(2) Typically accessed via CPU registers for low latency
  DMA network: 1-512 word data plane blocks Typically memory mapped
Reliable datagrams
  In-order delivery between any pair of endpoints
  Guaranteed minimum QoS for hard realtime systems

## Slide 11: Network-based access control
Provide CPU insn to send/recv message
Network accessed via formally verified transceiver IP
  Untrusted 3rd-party IP cores cannot spoof headers
  Neither can arbitrary code on the CPU
We can use packet headers for access control!
  Node can tell what app is accessing it
  Node makes access control decision based on msg origin

## Slide 12: IPC is now trivial
Each app already has a unique address on the NoC
Just send a packet to the app’s address

## Slide 13: Surely sbrk/malloc must be in ring 0…
Processor MMU provides translation only
You can map any phyaddr you want, but if the peripheral says “no” the app segfaults
mmap(2) no longer needs elevated privs!
  Just send a message to CPU OoB address

## Slide 14: Smart RAM controller
RAM controller has NoC API
  RPC: Allocate/free/chown page
  DMA: bulk read/write
App 1
RAM
Allocate
Page is 0x0800
App 1
CPU
Map ram:0x0800 at 0x41414000
OK

## Slide 15: Smart RAM controller
Trivially simple data structures
  FIFO of free pages
  Array of page owners
  Control state machine is ~500 lines including fluff
Easy to test / verify
  Thoroughly covered by automated test suite
  Formal verification in near future

## Slide 16: So what’s left in ring 0?
Nothing!
Remove privileged instructions from the ISA
Run userspace on bare metal
This is an antikernel – an OS with no kernel at all!

## Slide 17: Key concepts
This is not just a “hardware microkernel”
The “OS” is an emergent entity created from many independent state machines
These subsystems communicate in a limited, formally defined manner (complete encapsulation of state)

## Slide 18: Modularity for security
Each node maintains its own security state
Your TCB is what you make it
  A vuln in a node you don’t depend on has zero impact on your app’s security

## Slide 19: SARATOGA CPU
Compatible with mips GCC but not full MIPS
8 stage barrel processor, 200 MHz on Artix-7
  2 cycles each i-fetch, r-fetch
  4 cycles execution
2-issue in-order superscalar, 2N HW threads (N≥3)
Set-associative L1 cache, partitioned per thread
Hardware ELF loader w/ code signing
  HMAC-SHA256 for prototype to save FPGA resources
  Will use RSA or ECC in real system

## Slide 20: Name server
Resolve 8-char hostnames to 16-bit addresses
ROM of hard IP locations
Writable memory for software apps
  Signed updates to ensure authenticity

## Slide 21: Prototype implementation
~187 kLine including test cases, build tools, etc
Critical stuff is small
  RPC/DMA networks combined 4.5 kLine
  Name server 1 kLine
  SARATOGA CPU 9 kLine
All code is F/OSS (3-clause BSD)
Goal is to encourage reproduction of results, industry/academic research, etc

## Slide 22: Future work
Add more peripherals
Solve name binding problem for NVM
Formally verify non-reduced-payload DMA protocol
Formally verify SARATOGA (or its successor)

## Slide 23: Questions?